## Slide 1
IEE 802.11ax: Highly Efficient WLANs for
Intelligent Information Infrastructure
D. Deng, Y. Lin, X. Yang, J. Zhu, Y. Li, J. Luo and K. Chen
CHANGWON NATIONAL UNIVERSITY
2017 IEEE Communication Magazine

## Slide 2: Introduction
The world is experiencing extreme urbanization
  Wi-Fi Internet connections and hotspots to operate, significant growth
  Devices requires further technological break-throughs to meet the needs of high-density service
Wi-Fi(IEEE 802.11) plays a critical role in the infrastructure of cities
However, it has been 20 years since the first technical approval of the IEEE 802.11
  Highly efficient WLANs are therefore very much wanted to serve for future human society.

## Slide 3: Introduction
A new technology paradigm arises to revolutionize WLAN technology for UX
  Focusing on the performance metrics of multi-user on delay, latency and throughput
IEEE Standard Association approved IEEE 802.11ax in March 2014
  IEEE 802.11ax define standardized modifications to both the IEEE 802.11 physical (PHY) layer and medium access control (MAC) layer for high-efficiency operation
  Goal is to provide a better UX by improving by least 4 times the throughput per user
  In densely deployed environments

## Slide 4: Introduction
Key features
  Orthogonal frequency-division multiple access(OFDMA)
  Downlink / uplink multi-user multiple-input multiple-output
  Spatial reuse
  Trigger frame
  OFDMA random access
  Power saving with target wake time
  Station-to-station operation

## Slide 5: Introduction
This paper provide a brief overview of important PHY advancements in IEEE 802.11ax
Key technologies proposed for IEEE 802.11ax MAC to improve the efficiency of high density WLAN

## Slide 6: IEEE 802.11ax PHY
IEEE 802.11ax employs multi-user technology as PHY layer transmission in both up-link and down-link to serve more users at the same time.
Multi-user technology
  OFDMA: allowing simultaneous access to radio resource.
  Multiple user
  Multiple input/output
https://wballiance.com/wp-content/uploads/2019/07/Wi-Fi-6-Deployment-Guidelines-and-Scenarios-V1.0.pdf

## Slide 7: OFDMA PHY
OFMAD employs multiple subcarriers
  Subcarriers are divided into multiple groups
  Each group is referred to as resource unit(RU)
  RUs are allocated to multiple mobile stations according to their channel conditions and requirments
OFDMA reduces preamble and channel access overhead by distributing across several users
  Provide additional efficiency gain by assigning each user an RU

## Slide 8: OFDMA PHY
Access point may increase the power on some RU for maximize DL(downlink) throughput
Typically, STAs have lower output transmit power than APs
Power asymmetry reduces the UL(uplink) throughput
  UL OFDMA can be used to compensate for such power asymmetry

## Slide 9: Numerology and tone plan
In order to better serve OFDMA feature,
  The subcarrier spacing should be as small as possible to minimize the relative guard overhead
  Provide better frequency selective gain
IEEE 802.11ax supports 0.8us, 1.6us and 3.2us guard interval duration
  Cover a range of delay spread for indoor and outdoor channel

## Slide 10: Numerology and tone plan
IEEE 802.11ax defined for DL/UL transmission: 26-tone(subcarrier) RU ~ 2*996-tone RU
IEEE 802.11ax support 20, 40 and 80MHz bandwidth
  80 + 80MHz(non-contiguous) and 160MHz is also selectively available
RU location in 20MHz
RU location in 40MHz
RU location in 80MHz

## Slide 11: IEEE 802.11ax PPDU format
Four IEEE 802.11ax physical layer convergence protocol data unit(PPDU) format are defined
  Single-user PPDU(HE SU PPDU), HE: high efficiency
  Multi-user PPDU(HE MU PPDU)
  HE trigger-based PPDU
  Extended range transmission PPDU(HE ER SU PPDU)

## Slide 12: Preamble puncturing
In IEEE 802.11ax, 20 MHz, 40 MHz, 80 MHz, and 160 (80+80) MHz are supported in 5 GHz band
However real deployment 80 MHz and 160 MHz bandwidth channels may not be realistic to use
  Unlicensed spectrum in 5GHz is not contiguous
  Since the transmit power regulations are different in each band, for a BSS* that needs high transmit power the number of channels is further reduced.
  Radar spectrum overlaps with part of 5 GHz unlicensed spectrum, the channel cannot be used when radar signal is detected.
  The deployment of legacy APs operating at narrowband makes it hard for the AP to find a clear 80 MHz or 160 MHz bandwidth channel.
*Basic service set

## Slide 13: Preamble puncturing
IEEE 802.11ax support preamble puncturing that allowing an AP to transmit an HE MU PPDU in punctured 80 or 160 (80+80) MHz format when part of the 20 MHz sub-channel(s) in secondary channels of the channel bandwidth is busy.
Preamble puncturing is designed to enhance the channel utilization for the dense AP

## Slide 14: DL/UL MU-MIMO
IEEE 802.11ax introduces UL MU-MIMO, which improves the aggregate throughput of an IEEE 802.11ax network by parallelization of multiple transmissions on the UL
Both DL and UL MU-MIMO transmissions are supported on portions of the PPDU bandwidth
MU-MIMO support for up to eight users with up to four space-tine streams per user with the total number of space-time streams not exceeding eight.

## Slide 15: IEEE 802.11ax MAC
IEEE 802.11ax MAC design due to the multiple users sharing a frequency carrier/band, resulting in a new technology challenge in carrier sense
The basic idea is to leverage the concept of four way handshaking by establishing a trigger frame to allow efficient operation of multiuser PHY.

## Slide 16: UL MU procedure
UL MU transmissions leverage a new control frame called a trigger frame
  AP sends a trigger frame to multiple STAs to trigger them to transmit frames in MIMO
  After receiving the trigger frame and ensuring that it is one of the target STAs
  Each of the triggered STAs needs to complete the following in a fixed time slot