## Slide 1
Evaluation of the Minstrel Rate Adaptation Algorithm in IEEE 802.11g WLANs
Dong Xia, Jonathan Hart, Qiang Fu
CHANGWON NATIONAL UNIVERSITY
IEEE ICC’13

## Slide 2: Introduction
IEEE 802.11 standards specify multiple data rates
Data rate depending on the modulation and coding scheme used at physical layer
High data rate: fast data transmission, high bit error occurrence probability
Low data rate: longer data transmission, low bit error occurrence probability
Both are also affected by channel condition
IEEE 802.11g Data Rates Specifications,
Mikulka, Jan and Stanislav Hanus. “IEEE 802.11g baseband physical layer simulation.” (2007).

## Slide 3: Introduction
Wireless channel is extremely variable
Channel condition can be affected by a number of different factor
  Signal interference, multi-path fading, attenuation
Rate adaptation is crucial to wireless network performance
  Data rate optimization problem
  Fast data transmission, low bit error considering
  the channel conditions
https://www.everythingrf.com/community/what-is-signal-fading

## Slide 4: Introduction
A lot of research has been done for the effective data rate adaptation algorithm.
  RRAA, ARF, AARF, WOOF, etc.
  Minstrel is a recently-developed adaptation algorithm
Performance evaluations of Minstrel are scares
This paper present analysis the performance of Minstrel in real-world IEEE 802.11g

## Slide 5: Minstrel algorithm
Minstrel algorithm consists of three parts
  Retry chain mechanism
  Rate decision process
  Statistic calculations
Retry chain mechanism
  Retry chain react to variations in channel quality
  Four rate-count pair ()
  data rate
  c: unsuccessful transmission attempts
1
1
2
2
3
3
Sender
Receiver
AP
If transmission fail
1st retransmission attempt
2nd retransmission attempt
3rd retransmission attempt
How to determine -value?
High
Transmission stability
High
Transmission speed

## Slide 6: Minstrel algorithm
Rate decision process
  Minstrel algorithm have two categories of transmission
  Normal transmission: 90% of packet transmission at entire time
  Sampling transmission: 10% of packet transmission at entire time
Normal transmission
  : Set to the highest expected throughput
  : Second highest expected throughput
  : Highest probability of success of transmission
  : Lowest rate of available

## Slide 7: Minstrel algorithm
Sampling transmission
  : Set to higher sample rate or highest expected throughput rate
  Sample rate: random generated data rate
  : Whichever is lower rate
  , : remain rate with the highest probability of success and lowest rate
How to calculate expected throughput and successful probability?
  Statistics calculation
  EWMA(Exponentially Weighted Moving Average)

## Slide 8: Minstrel algorithm
Statistics calculation
  Minstrel maintains the probability and expected throughput for each data rate as EWMA
  Probability is used to estimate the throughput
  Throughput expectation of each rate recalculated per 100ms (sampling window)

## Slide 9: Minstrel algorithm
EWMA
  : success rate at current window
  : number of packets transmitted successfully
  : total number of packet
  : determine how much weight is given to the (default:0.25)
  ↑current success rate is highly reflected to next probability
  Next probability = current success rate x (1- 0.25) + current probability x 0.25

## Slide 10: Minstrel algorithm
Throughput expectation
  number of byte, raw throughput of rate
  Success probability x (/t)

## Slide 11: Minstrel algorithm
Calculate each rate’s throughput expectation per 100ms
  In sampling transmission, random rate is also calculated
throughput expectation comparing
  As rate select policy, r0 ~ r3 rates are selected

## Slide 12: Evaluation
Testbed
  Send UDP traffic from the sender PC to a laptop receiver
  AP used 802.11g mode
Comparing case
  Fixed data rate
  Minstrel
Send UDP traffic using iperf

## Slide 13: Evaluation
Test case
  Static channel: static channel quality
  Rapid channel variation: channel quality will jump from good to poor quickly
  Gradual channel variation: channel quality will change gradually
  Channel quality can control by AP’s transmission power(mW)

## Slide 14: Result
Rate selection breakdown

## Slide 15: Result
Rate selection breakdown