## Slide 1
Perceptron Learning for Reuse Prediction
Elvira Teran, Zhe Wang, Daniel A. Jimenez
CHANGWON NATIONAL UNIVERSITY
MICRO’16

## Slide 2: Perceptron Learning
Perceptrons
  A simple model of neurons in neural networks
  Online training
  Output – the dot product of the weights and a vector of inputs
In the paper, they do not actually use perceptron.
  Use the perceptron learning algorithm
Use perceptrons to make prediction for LLC cache replacement.

## Slide 3: Perceptron Learning
The perceptron learning algorithm
  Some criteria for choosing a vector of signed weight
  If exceeds some threshold, the prediction is true.
  If the prediction is wrong, the inputs are used to update the weights.
Indexing independent tables
  Choosing the weights
Hashed perceptron predictors
  Compute a sum, instead of a dot product

## Slide 4: Contributions
Perceptron learning can improve accuracy of reuse prediction
  With combine multiple inputs
Outperforming the SOTA policies for both single and multiprogrammed workloads
More than doubles cache efficiency over the LRU
Evaluates with considering prefetching

## Slide 5: Features
The trace of memory access instructions
  Keep tracks of recent PCs accessing the LLC
The PC of the memory instruction
  The succinct proxy of the block
Bits from the memory address
  The page number or tag
A compressed representation
Time/reference count

## Slide 6: The Main Idea
Each feature is indexed a distinct table.
If the sum exceeds some threshold, the prediction is “not to be reused”
Sampler for updating the predictor
The prediction is incorrect, then the weights are decremented on an access

## Slide 7: The Main Idea
Combining features by summing weights
  Avoid destructive interference and exponential blowup
Using the perceptron update rule
  The predictor adapt to changes in program behavior.

## Slide 8: The Main Idea
The recent reuse predictors (SDBP, SHiP)
  A single feature

## Slide 9: The Main Idea
The perceptron-based reuse predictor
  Each feature is hashed
  XORed with the PC to index a separate table
  Discovers correlation and ignores the lack of correlation

## Slide 10: Example
Load A - predicted well by a PC-based predictor
Load B – predicted well by a page-based predictor
Perceptron learning separates the two features into two different tables.

## Slide 11: Training with a Sampler
A separate array for a small number of sampled sets
A partial tag
  To identify the block
representing the most recent prediction computation
  Used for threshold rule of the perceptron learning algorithm
A sequence of hashes of the input features
  Used to index the prediction tables
LRU bits for replacement within the sampler

## Slide 12: Predictor Organization
A set of tables, one per input feature
Each table with 256 entries of 6-bit signed
weights

## Slide 13: Making a Prediction
When there is an access to the LLC
When an incoming block is considered for placement in the LLC
Each cache block with its most recent reuse prediction used to drive the replacement policy

## Slide 14: Training the predictor
When there is a replacement in the sampler,
  The eviction of the LRU entry shows it is unlikely to be reused.
When a sampled entry is accessed,
  The current set of features is correlated with reuse.
The predictor learns from these evidences.

## Slide 15: A Replacement and Bypass Optimization
Tree-based PseudoLRU as the default replacement policy
When a block is hit in the LLC,
  The predictor is consulted using the current vector of features.
When there is a miss in the LLC,
  The predictor is consulted to predict whether the incoming block will have reuse.
  If it is predicted to have reuse, a replacement candidate is chosen.
  The set searched for a block predicted not to have reuse.
  Otherwise, the block chosen by the PseudoLRU policy evicted.

## Slide 16: Prefetches
When the hardware prefetcher attempts to bring a block,
  The predictor makes a reuse prediction for that block.
  A single fake address is used for all prefetches for hashing

## Slide 17: Methodology
Performance models
  An in-house simulator
    32KB 8-way L1 cache
    256KB 8-way L2 cache
    200 cycles DRAM latency
  An out-of-order 4-wide 8-stage pipeline with a 128-entry instruction window.
  4MB L3 cache for single-thread simulations
  16MB L3 cache for multi-core simulations
  A stream prefetcher

## Slide 18: Methodology
Workloads
  The 29 SPEC CPU 2006 benchmarks
  SimPoint to identify up to 6 segments of one billion instructions

## Slide 19: Results
Multi-Core Results
  Performance
    The weighted speedup
    Mean
      Perceptron : 7.4%
      SDBP : 4.3%
      SHiP : 4.4%

## Slide 20: Results
Multi-Core Results
  Miss
    y-axis : log scale
    Mean (percentage over LRU)
      Perceptron : 7.2MPKI
      LRU : 9.4MPKI
      SDBP : 7.8MPKI
      SHiP : 7.6MPKI

## Slide 21: Results
Without Prefetching
  Accuracy
    Coverage (Lighter)
      The percentage of all predictions
      for which a block is not to be reused
    False positive (Darker)
      The potential cache misses
    The coverage of perceptron is higher.
    The false positive of perceptron is lower.

## Slide 22: Results
Single-Core Results
  Performance
    Single-thread speedup
    Mean (percentage over LRU)
      Perceptron : 6.1%
      SDBP : 3.5%
      SHiP : 3.8%

## Slide 23: Results
Single-Core Results
  Miss
    4MB LLC
    y-axis : log scale
    The average MPKI figures are low
      Most of the benchmarks fit working sets
      into a 4MB cache.

## Slide 24: Results
Cache Efficiency
  The fraction of time that a given cache block is live
  Lighter means better efficiency

## Slide 25: Results
Analysis
  Perceptron learning improves accuracy over previous techniques.
  Wider weights and more features allow more correlations to be find.

## Slide 26: Conclusion
Finding independent correlations between multiple features
Better than previous work
The complexity is not worse