## Slide 1
Towards SLO Complying SSDs
Through OPS Isolation
Jaeho Kim, Donghee Lee, Sam H. Noh
CHANGWON NATIONAL UNIVERSITY
FAST ‘15

## Slide 2: Idea Summary
Performance SLOs cannot be satisfied with current commercial SSDs
  At I/O bandwidth distribution, Proportionality deviation is worse for SSD than HDD
  Garbage Collection(GC) interfere among VMs.
GC overhead is increased by containing pages from various workloads at same block
  GC cost is main factor of IOPS
Reducing GC overhead, dedicate OPS memory block to each VM separately
  Scheme called 'OPS Isolation' can prevent same block mixed by different workload's pages
  OPS memory size is dynamically adjusted per VM's IO weight

## Slide 3: Strength & Weakness
Strength
  OPS Isolation reduces Garbage Collection cost by isolating OPS blocks per VM
  Cgroup subsystem for weight based I/O distribution to function properly in SSD by OPS Isolation
Weakness
  Couldn't find detail for how dedicate memory block including OPS for each VM separately
  There is hard to guarantee that ops isolation shows the same performance in commercial SSD