## Slide 1
MLCache: A space-Efficient Cache Scheme based on Reuse Distance and Machine Learning for NVMe SSDs
Weiguang Liu, Jinhua Cui, Junwei Liu, and Laurence T. Yang
CHANGWON NATIONAL UNIVERSITY
ICCAD’20

## Slide 2: NVMe
A promising solution to replace the conventional SATA in modern SSDs
Modern NVMe SSDs provide the diverse multiple streams on the cache.
MLCache is a space-efficient shared cache management scheme for NVMe SSDs.

## Slide 3: Cache scheme
In previous study,
  A global shared cache
  Simple and convenient, but it fails to deal with the phenomenon of performance interference.
  A statically partitioned cache
  Avoiding performance interference, but the valuable cache resource may be underutilized.
  Partitioned cache space is inflexible.
MLCache
  Use artificial neural network to learn and predict the optimal cache space allocation scheme
  A solution to dynamically divide the cache space

## Slide 4: Reuse distance
The cache hits mainly depend on the relationship between the requested reuse distance and the cache size
Sub-problems
  How to obtain the reuse distance and relative frequency of each stream request
  How to build a model based on quantified locality and frequency to obtain the optimal solution

## Slide 5: Artificial neural networks
ANN can automatically learn to approximate the target model
MLCache use artificial neural networks to model cache allocation based on reuse distance

## Slide 6: MLCache architecture
Reuse distance monitoring module
  Continuously monitor each stream’s request address
  Analyze the reuse distance and relative frequency
Neural network module
  Input: the reuse distance and relative frequency
  Output: the allocated space of each stream
  Can get a space-efficient cache scheme

## Slide 7: MLCache
MLCache solves two problems:
  How to describe the reused distance distribution of the stream to form input data
  How to predict the optimal allocation scheme based on the data obtained in the first problem

## Slide 8: MLCache
Monitor
  Use PARDA to calculate the reuse distance
  Use the nearest reuse distance as a reference
  Recent Queue
    An additional queue to store the reused distance of the last N requests
    The stream identification and reuse distance are collected in Recent Queue.
    N should be selected based on the longest fluctuation period of the flow.
    Counts Recent Queue to obtain the frequency of k streams in all used distance intervals
  [] records the frequency of each stream in each reused distance interval segment.

## Slide 9: MLCache
The algorithm flow of the reuse distance module

## Slide 10: MLCache
Artificial neural network
  Offline mode
  To reduce the access latency, deep neural network doesn’t contain lots of neurons
  [] as input in the previous section, real optimal distribution solution as a label for training
  The loss is set as the squared difference
  Penalty factor for exceeding the constraints

## Slide 11: MLCache
The algorithm of the neural network module

## Slide 12: MLCache
The cache module changes the space size according to the optimal allocation scheme.
For the expanded cache size,
  The capacity of the stream directly set to the allocated size
For the reducing cache size,
  Using LRU method to evict
  Evict one cache page at a time until the cache size of the stream reaches the size
Allocate according to the equal space distribution for abnormal allocations

## Slide 13: MLCache
Overhead analysis
  Space overhead
    The maximum space complexity of PARDA is O(M)
    The Recent Queue only use 1 byte to for stream id and 2 bytes for reuse distance
    The space occupied by the reused distance distribution can’t exceed 2KB
  Computation overhead
    The time complexity of the reuse distance is O(log M)
    The neural network is trained offline, and the neural network is used for calculation at the end of a period, so the delay caused by the overhead is small

## Slide 14: Experiment
Trace-driven SSD simulator, MQSim
256GB capacity NVMe flash-based SSD
Supports up to 8 streams for simultaneous reading and writing
Use different cache capacities to simulate scenarios
  260 pages in the 4-streams
  680 pages in the 8-streams

## Slide 15: Experiment
Using 16 real enterprise server traces
Using 2 streams, 4 streams, 8 streams for testing
  ¼ of real traces, and added synthetic traces
Calculate the optimal solution through the simulator
In the experiments, following schemes are implemented
  Evenly partition (baseline)
  MLCache
  Discrete optimal partition (ideal)

## Slide 16: Experimental Results
Hit ratio

## Slide 17: Experimental Results
Hit ratio
  MLCache is suitable for different capacities.
  The effect of improving the hit rate is more obvious when the cache capacity is scarce.
  The improvement of the cache hit comes from:
    Request local changes
    Changes in the size of the cache space
  All traces have a larger improvement in hit rate compared to baseline.
  All are close to discrete optimal partition.
  The smaller the number of streams, the more the MLCache approaches the optimal solution.

## Slide 18: Experimental Results
Response time
  MLCache can effectively dynamically allocate the optimal cache space for each stream.

## Slide 19: Conclusion
MLCache allocates efficient cache space for each I/O queue independently according to the reuse distance distribution and relative request frequency.
MLCache is 96% similar to the ideal model.