## Slide 1
Frequent Access Pattern-based Prefetching Inside of Solid-State Drives
Xiaofei Xu, Zhigang Cai, Jianwei Liao, Yutaka Ishiaka
CHANGWON NATIONAL UNIVERSITY
DATE’20

## Slide 2: Data prefetching
Data prefetching is for reducing the overhead of read operations
Previous prefetch scheme involved with the OS layer
  Damage compatibility and transparency
Previous prefetch scheme inside SSDs
  Confined limited resources
  For only a few application scenarios

## Slide 3: Data prefetching
Prefetching inside SSDs
  OS-independence
  Transparency
The division of write/read cache should depend on real-time workloads

## Slide 4: This paper,
A frequent access pattern-based prefetching scheme
An adaptive cache management policy
  Separately buffering the write data and the prefetched data in SSDs
  Based on I/O workloads characteristics

## Slide 5: System architecture
Cacher at FTL
  RAM division
  Pattern mining
  Read prediction
Default garage collection policy & wear-leveling policy

## Slide 6: Pattern-based prefetching
Identifying and modeling frequent access patterns
  FP-Growth algorithm
A set of logical addresses of requests
A, B, C, D
B, C, D, E
B, C, E
A, C
{B, C, D}
{B, C, E}
Union
{B, C, D, E}
B, C, D : 2
B, C, E : 2
A, C : 2

## Slide 7: Pattern-based prefetching
Pattern matching for data prefetching
  A matrix to reflect the relationship between the logical sector numbers and the patterns
  The prefetching trigger condition is about more than a half of LSNs accessed
  Example
    0, k, k+1 were requested

## Slide 8: Adaptive cache management
Adaptively separate the cache for written/prefetched data
Dynamically adjust cache use on the several factors
  The numbers of read and write requests
  The size of read and write space
  The numbers of read and write hits in cache
  in the previous time window

## Slide 9: Adaptive cache management
Determine the prefetch enabled or nots
  If τ >= predefined value, the prefetch disabled
Calculate the ratio of SSD cache for holding the prefetched data
LRU for ejecting a corresponding page of data

## Slide 10: Experiment setup
SSDsim
4 disk traces from Microsoft Research Cambridge traces
Schemes
  Baseline(no prefetching)
  Lynx
  Resource-Optimized Prefetching(ROP)
  Pattern (proposed scheme)

## Slide 11: Read response time
Pattern can reduce the read latency
Hm_0
  All prefetching scheme is worse than baseline
  60.1% hot read addresses = hot write addresses
  Many small read requests less than the prefetching unit
  Pattern is similar to baseline

## Slide 12: Overall I/O time
Prefetching must place negative effect to the performance of write data
The overall I/O time shows effectiveness of prefetching
Pattern outperforms others excluding hm_0

## Slide 13: Prefetching hit per prefetch
Patterns yields the best outcomes

## Slide 14: Cache use efficiency
(the total read hits) * (the read time – the read hit time) + (the total write hits) * (the write time – the write hit time)
The proposed scheme improve cache use efficiency by up to 21.1%

## Slide 15: Analysis on adaptive cache partition
Lynx, ROP
  a fixed 8% cache for buffering the prefetched data
Proposed scheme takes advantage of different ratios for different traces

## Slide 16: Summary
The proposed scheme can cause a higher accuracy in forecasting
  by avoiding unnecessary prefetching operations
Adaptive cache management scheme dynamically adjust the cache partition
  to boost the efficiency of cache use
The proposed scheme reduce the time required by prefetching

## Slide 17: Conclusions
An OS-independent data prefetching mechanisms for SSDs
The proposed scheme can reduce I/O response time by up to 9.1% on average
The adaptive cache partition policy can enhance the cache use efficiency by up to 21.1%