## Slide 1
HAML-SSD: A Hardware Accelerated
Hotness-Aware Machine Learning based
SSD Management
Bingzhe Li, Chunhua Deng, Jinfeng Yang, David Lilja, Bo Yuan, David Du
CHANGWON NATIONAL UNIVERSITY
ICCAD’19

## Slide 2: Introduction
Garbage collection
  Extra writes and causes large overhead
HAML-SSD
  Hotness-Aware Machine Learning based SSD management
  Reduce the overhead of GCs in SSDs
  K-Means algorithm
  Define the “hotness” of a data page by clustering data with I/O access patterns

## Slide 3: Introduction
Contributions
  Update frequency, average update time interval
  Machine learning method
  A hardware unit, HAML-unit is designed to accelerate the machine learning algorithm
  Analyze trade-offs between different values of parameters

## Slide 4: Motivation
GC causes a large migration overhead
Previous works
  Only defined the hotness by the update frequency
  A constant threshold to partition data pages into hot and cold
HAML-SSD
  Also consider about the average update time interval
  Capable of dynamically classifying data access patterns by using ML

## Slide 5: K-Means
Unsupervised learning
  There is no ground truth to indicate which class they should belong to
K-Means
  Sumpler, faster and more flexible

## Slide 6: HAML-SSD Design
Overall architecture
  UpdateF_TBL
  UpdateT_TBL
  K-Means unit
    The hardware implementation of the K-Means algorithm

## Slide 7: HAML-SSD Design
ML allocation policy
  Parameters
    Update frequency
    Average update time interval
  Slices
    Split the SSD logical address into smaller contiguous regions called slices
    The SSD records two parameters for each slice in each time period
  Two-dimension K-Means clustering algorithm

## Slide 8: HAML-SSD Design
Major functions
  Scheduling
  Monitoring
  K-Means clustering
  Hot_Q, Cold_Q for wear-leveling

## Slide 9: HAML-SSD Design
ML unit design
  K-means clustering algorithm is time-consuming

## Slide 10: Experiment
Environment setup
  Greedy GC scheme
  GC activation threshold is set to 128 free blocks
  SSDsim simulator
  Cambridge MSR traces, Systor’17 traces
  K-Means cluster will be re-trained every 6 hours

## Slide 11: Experiment
HAML-SSD hardware implementation
  Sysnopsys Design Compiler to synthesize the design with the TSMC 28nm technology
Execusion time comparison

## Slide 12: Experiment
Overall performance comparison

## Slide 13: Experiment
Overall performance comparison

## Slide 14: Experiment
Varying number of clusters
  A large number of clusters has a higher ability to classify a lower number of cluser distribution

## Slide 15: Experiment
Performance with varying slice size
  Ts_0, prxy_0 have obvious difference in small slice size
  proj_1, LUN0 are not sensitive to the slice size
  Web_2 does not have enough update information for small slice sizes in one time period
  Smaller slice sizes might provide better I/O performance but cause longer execution time

## Slide 16: Experiment
Performance with varying T
  Usr_2, prxy_0 have similar update patterns for different T
  LUN0, LUN3 have significantly changed access patterns for differen T
  A shorter time period will cause more training, a trade-off between the time period and clustering execution time

## Slide 17: Conclusion
HAML-SSD to improve the garbage collection efficiently
  Update frequency, update time interval
  K-Means clustering algorithm
  HAML-unit is designed in the SSD, which reducing overhead
HAML-SSD reduces the response time compared to previous works
Investigation about different design parameters