## Slide 1
File Fragmentation in Mobile Devices: Measurement, Evaluation, and Treatment
Cheng Ji, Li-Pin Chang, Sangwook Shane Hahn, Sungjin Lee, Riwei Pan, Liang Shi, Jihong Kim, Chun Jason Xue
CHANGWON NATIONAL UNIVERSITY
IEEE Transaction on Mobile Computing

## Slide 2: Introduction
I/O efficiency is among the key factors that affect the overall responsiveness of mobile devices
File fragmentation
  The progressive response time degradation in mobile devices
The goals of this study
  To understand how bad file fragmentation in Android devices is
  How fragmentation is produced
  How fragmentation impacts on user-perceived latencies
  The dfficacy and limitation of existing methods of fragmentation management

## Slide 3: Introduction
Fragmentation measurement
  How bad file fragmentation is in real smartphones
  Identified file fragmentation is closely related to the file access & I/O behaviors
  Designed AutoAge tool for systematically ages a file system in a reproducible manner
Evaluation of performance impact
  How fragmentation impacts on user-perceive latencies of mobile apps
  Launching time, installing time, SQLite query processing time
Fragmentation treatment
  The efficacy and limitation of existing methods for fragmentation treatment
  Space allocation, persistent journal, file defragmentation

## Slide 4: Fragmentation in File Systems
File fragmentation
  File contents are not entirely stored contiguously
  Amplifies the disk seek frequency
  Degrades the performance of HDD storage systems
File deletion
  Leaves non-contiguous free space in the file system

## Slide 5: Fragmentation in File Systems
File fragmentation in SSDs
  Common belief: file defragmentation has little effect on SSDs, but harmful to SSD lifespan
  Conway et al. Observed that the read performance of data servers could severly degrade due to poor file layouts on hard disks or SSDs
In this study, they found that file fragmentation is a serious problem in real smartphones

## Slide 6: File Defragmentation
E4defrag
  A file defragmentation tool for Ext4 file system
  Creates a large sequential donor file, copies data from the fragmented file to the donor file
  Based on data copying

## Slide 7: A Empirical Study of Real Smartphones
Setup
  Daily use – including Facebook, Twitter, Chrome, Gmail, Camera, Google Earth

## Slide 8: A Empirical Study of Real Smartphones
Degree of Fragmentation (DoF)
  As a major evaluation metric
  {The number of extents allocated to the file x} / {The ideal number of extents necessary for the file x}
  A single extent can cover up to 128MB in Ext4
Fragment Size (FS)
  File fragmentation has a larger performance impact on small fragments than larger ones

## Slide 9: A Empirical Study of Real Smartphones
File system snapshot analysis
  The higher the file system space utilization was, the more files were fragmented N5 (high space utilization: 93%)
  Files in older smartphones tend to be more fragmented S3 (2 years), N6 and P7 (no more than one year)

## Slide 10: A Empirical Study of Real Smartphones
File system snapshot analysis
  Whether fragmentation is correlated with file types
  45% of the fragmented files were SQLite files
  Non-SQLite files were fragmented in aged file systems

## Slide 11: File Fragmentation Reproduction
Scenario-driven application replay
  Developed a UI testing tool AutoAge based on the UIAutomator framework
  Applications installing, updating, running

## Slide 12: File Fragmentation Reproduction
Scenario-driven application replay
  The space fullness was not high on the first day, but the DoF of SQLite files was already high as 3
  From the 11th day, the fragmentation of SQLite files progressively developed as the File system aging

## Slide 13: File Fragmentation Reproduction
Scenario-driven application replay
  DoF of Multimedia and Executable files noticeably increased on the 11th day and onward because file system is nearly full

## Slide 14: File Fragmentation Reproduction
Scenario-driven application replay
  The number of fragments of the smallest FS level significantly increased on the 11th day
  Free space was severly fragmented into small holes when the file system is was nearly full

## Slide 15: File Fragmentation Reproduction
Multi-Threaded SQLite Operations
  When the total number of concurrent threads was large, small fragments from different files were severely interleaved with one another
  File fragmentation is also a sever problem in IOS

## Slide 16: File Fragmentation Reproduction
Causes of fragmentation
  Impact of high space utilizations
  SQLite files of Google Earth were much larger than those of Facebook

## Slide 17: File Fragmentation Reproduction
Causes of fragmentation
  Impact of write behaviors
  Even when the space utilization was Low, DoF of SQLite files were high
  This result is closely related to frequent deletion of journal files & concurrent writing to DB files

## Slide 18: File Fragmentation Reproduction
Causes of fragmentation
  Impact of storage capacity
  No matter how large the storage device was, the SQLite files were still badly fragmented
  Using a large storage device or decreasing the file system space utilization effectively avoids fragmentation of non-SQLite files, but it has no effect on SQLite files

## Slide 19: Performance Impact
A basic performance model
  The correlation between the time overhead of accessing file and the DoF of the file
  The latency linearly increased with the DoF value
  The latency slightly dropped when the DoF increased 1 to 400 related to the internal data placement of the eMMC device

## Slide 20: Performance Impact
User-perceived latencies
  Application launching
  File fragmentation contributes to user-perceived latencies of application launching

## Slide 21: Performance Impact
User-perceived latencies
  Application installing
  File fragmentation contributes to user-perceived latencies of application installing

## Slide 22: Performance Impact
User-perceived latencies
  SQLite query processing
  File fragmentation contributes to user-perceived latencies of application installing

## Slide 23: Causes of Performace Impact
Increased block I/O frequency
  Accessing fragmented files would result in an increased I/O frequency
  Blktrace
  The block I/O count with file fragmentation was significatly higher than that without fragmentation (47,570 vs 812)
  This amplified block I/O frequency increased the total time of file reading by 1.6 seconds

## Slide 24: Causes of Performace Impact
Dispersed I/O pattern
  The larger the write region, the more dispersed the write operations in the storage spac
  The total write times on P7 & S3 with the largest write region were slow
  On N5, N6, the total write time is less sensitive to the write region size

## Slide 25: Causes of Performace Impact
Pattern-induced I/O pattern
  Closely related to the logical-to-physical map caching mechanism inside of mobile flash storage
  A large cache size (128 KB), a small cache size (16 KB)
  The I/O region was enlarged, both read and write time increased
  GC amplified the overhead of cache miss management

## Slide 26: Fragmentation Treatment
Space preallocation
  When the number of threads was large at the low space utilization level, file fragmentation was completely eliminated using space preallocation with units of 512 KB
  DoF values under high space utilization were higher than those under low space utilization

## Slide 27: Fragmentation Treatment
Space preallocation
  Attempt to find a proper preallocation size for SQLite files of real mobile applications
  When the preallocation size was 128 KB, at least 83% of SQLite files were not fragmented

## Slide 28: Fragmentation Treatment
Persistent journal
  In PERSIST mode, journal(.db-journal) were lightly fragmented because they were written as a whole and barely grew DB files were badly fragmented because of the concurrent frequent growth of multiple db
  In WAL mode, journal(.db-wal) were badly fragmented because of the same reason above DB files were lightly fragmented because of large batch writes

## Slide 29: File Defragmentation
Conventional defragmentation (e4defrag)
  Copy-based
  Find as large extents as possible and re-locate the fragments of the file to the large extents
  Ideal DoF
  A fragmented file still has a DoF value larger than 1 after defragmentation with e4defrag when e4defrag cannot find a sufficiently large extent

## Slide 30: File Defragmentation
Conventional defragmentation (e4defrag)
  When the file system space utilization was low, e4defrag eliminated all file fragmentation
  E4defrag decreased the average DoF only by ½ compared to no defragmentation with 10 threads

## Slide 31: File Defragmentation
Copyless defragmentation
  The data copying introduces extra write stress to mobile storage
Janusd
  For defragmenting files on flash-based mobile storage
  Exploit the existing logical-to-physical mapping in the firmware layer inside of mobile storage
  Remap existing data in flash memory from fragmented logical addresses to continuous ones
  Modifies the mapping information inside of mobile storage
  No data copying

## Slide 32: File Defragmentation
Janusd
  The same average DoF values as e4defrag
  Janusd is based on the same defragmentation logic as that of e4defrag
  Write stress reduction: 98% fewer flash writes than e4defrag did

## Slide 33: Conclusion
Examined how severe file fragmentation is in real mobile devices
  How fragmentation negatively impacted user-perceived latencies
  The increased block I/O frequency and defraded device mapping cache efficiency
Evaluated existing methods for fragmentation treatment
  File defragmentation (conventional and copyless) is useful to write-once files
  Space allocation is effective on SQLite files